SimulationRun
UserCommands
The controlling class – it generates all the components of the optical train, reads in the science cube, then applies each optical effect in turn.
Input: UserCommands
Attributes: ...
Methods:
read_user_comands(str filename)
import_science_object()
generate_optical_train()
make_rocket_go_now()
A dictionary that contains all the parameters needed by SimulationRun. These include all aspects related to the optical train, input cube and observation strategy.
add_atmosphere()
apply_psf()
apply_throughput()
add_blackbody_emission()
collapse()
apply_plane_effects()
make_detector_image()
OutputImage
ThroughputCurve
Input: UserCommands
Attributes: lam, val, lam_res
Methods:
from_skycalc(str filename)
from_file(str filename)
from_list(list ThroughputCurve)
resample(arr lam)
Operators: *
PSFCube
Input: UserCommands
Attributes: lam_edges, lam_centres, psf_cube, psf_list, size, fwhm, pix_res, weight_map
Methods:
generate_cubes()
combine_cubes()
Subclasses:
PSFCubeADC
PSFCubeFromFile
PSFCubeAnalytic
AtmosphericModel
Input: UserCommands
Attributes: TC, EC, Temp, Pres, %Hum, z0, lat, long, height
Methods:
read_skycalc(str filename)
read_tc(str filename)
read_ec(str filename)
get_photons(arr lam)
ScienceObject
Input: UserCommmands
Attributes: filename, image_cube, lam_edges, lam_centres
Methods:
convert_to_photons()
add_atmosphere(AtmosphericModel)
apply_psf(PSFCube)
apply_field_variant_psf([PSFCube])
apply_throughput(TransmissionCurve)
add_blackbody_emission(EmissionCurve)
collapse()
apply_plane_effects(PlaneEffect)
make_detector_image(Detector)
EmissionCurve
Input: UserCommands, TransmissionCurve
Attributes: lam, val, lam_res, tc, mirror_area, pix_res, energy_units
Methods:
from_skycalc(str filename)
from_file(str filename)
photons_per_bins(arr lam)
resample(arr lam)
Operators: *
PlaneEffect
Input: UserCommands
Attributes: pix_res, effect_type, kernel, shift_x, shift_y, stretch_x, stretch_y, theta, distortion_map, weight_map
Methods:
read_dist_map()
Notes: Types of effect: rotation, distortion, shift, convolution
Detector
Input: UserCommands
Attributes: shape, dark_mean, dark_stdev, from HXRGNG package; rd_noise, pedestal, c_pink, u_pink, can, pca0_amp
Methods:
generate_noise()
load_noise_frame(str filename)
save_noise_frame(str filename)
Notes: Dark noise is not generated by HXRGNG.
OpticalTrain
(Telescope + Instrument)
Input: UserCommands
Attributes: ...
Methods:
make_optical_train()
read_psf_cube()
generate_psf_cube()
write_psf_cube()
generate_transmission_curve()
generate_emission_curve()
generate_plane_effect()
read_detector_noise()
generate_detector_noise()
write_detector_noise()

---
Simput
Point sources
List x,y,mag,spectrum
Extended sources
n x ASCII spectrum
n x 2D intensity map
Extended sources
n x 2D images

---
File structure
SimCADO
scripts
Usage examples for SimCADO for MICADO/EELT and possibly other telescopes
user_commands
Holds the config files with all the editable parameters.
Input
The default folder for an input science data files – ASCII or FITS
output
Any files generated during a simulations are saved here by defaults. This path can be defined by the user
data
Holds data for the simulations
SimCADO
Holds the scripts that build up the SimCADO module
Master
Contains only the paths to the other config files
- master.config
Frequently used parameters
Contains any parameters that the user wants to play with. Overrides the default values.
- user.config
Atmosphere
Contains information relevant to functions that deal with the atmosphere
- atmosphere.config
Telescope + Instrument
Contains the parameters that control how SimCADO builds the optical train from M1 to just infront of the detector
- telescope.config
Detector characteristics
Contains parameters to do with the detector. Primarily those for the NG_HxRG module
- detector.config
Simulated Observations
Contains parameters relevant to a single simulated observation
- observation.config
Transmission Curves
ASCII files containing 2 columns:
wavelength [um], value [0...1]
- TC_filter_I.dat
- TC_filter_z.dat
- TC_filter_Y.dat
- TC_filter_J.dat
- TC_filter_H.dat
- TC_filter_Ks.dat
- TC_filter_K.dat
- TC_mirror_mgf2agal.dat
- TC_detector_H4RG.dat
SkyCalc Curves
A FITS binary table generated by the ESO skycalc online tool. The 3 interesting columns are lam, flux, trans
- skytable.fits
PSF files
A FITS cube containing PSFs for a specific mode over a specific wavelength range
- PSF_MAORY_Ks_0.6arcsec.fits
Detector files
Files needed by the NG_HxRG script to simulate the detector noise and examples thereof
- FPA_nirspec_pca0.fits
- FPA_detector_noise.fits
Scripts that contains all the modules for the SimCADO.
- Detector.py
- LightObject.py
- OpticalTrain.py
- SpectralCurve.py
- SimulationRun.py
- PlaneEffect.py
- PSFCube.py
- utils.py
See the package model
Temporary instrument files
Files which are generated during a simulation which can be used again to save time
- slices.fits
PSF slices per a filter range
- H4RG_noise.fits
If the detector pattern is re generated
- light.fits
Detector output
Simulated detector readout arrays are saved here. Various stages of the journey through the optical path can be saved
- output.clean.fits
- output.noise.fits
- output.raw.fits
- output.red.fits
.clean is only the source passing through
.noise is only the background noise
.raw is the combined source+noise
.red is the raw output minus a constant BG

---
AiryDiskDiff2DPSF(PSF)
...
Amplitude – float
eps – float
radius – float
position – float
AiryPSFCube(PSFCube):
...
diameter	– float
fwhm	– float
obscuration	– float
AiryPSF(PSF):
...
fwhm – float
CombinedPSF(PSF):
...
CombinedPSF(PSF):
...
DeltaPSF(PSF):
…
position – 1D array
DeltaPSF(PSF):
...
position	– float
PSFCube(object):
psf_slices	– list(PSF)
lam_bin_centers	– 1D array
info	– dict
GaussianPSF(PSF):
…
diameter – float
fwhm	– 1D array
PSF(object):
array	– 2D array
info	– dict
pix_res	– float
size	– float
GaussianPSF(PSF):
...
fwhm – float
MoffatPSF(PSF):
…
diameter – float
fwhm	– 1D array
MoffatPSF(PSF):
...
fwhm – float
UserPSF(PSF)
...
filename – str
fits_ext – int
UserPSF(PSF)
...
filename – str
fits_ext	– int
UnityCurve(TransmissionCurve):
…
val	– float
TransmissionCurve(object):
lam	– 1D array
val	– 1D array
lam_res – float
LightObject(object):
EmissionCurve(TransmissionCurve):
…
area	– float
pix_res	– float
exptime	– float
val_unit	– astropy.unit
BlackbodyCurve(EmissionCurve):
…
temp	– float